## Slide 1: Problem Statement: Hardware Design Engineer for Payload Electronics Development
Design of a high-accuracy Peizo-actuator control electronics for an Earth Observation (EO) payload.

## Slide 2: 1. Piezo Actuator
Actuator Specs
  Full stroke length: 400 micrometers
  Tip/tilt angle: 1 degree
  Precision of actuation: 100 nanometers
P/N : P-FSM400MML Fine Steering Mirror

## Slide 3: 2. Piezo Actuator Driver
  Actuator Drive specs
  Drive Voltage Range: -20 V to +150 V
  Load Impedance: 15 pF
  Peak power: <5 W
  Supply voltage: 5 V DC
  DAC resolution: 12 bits
  Linearity error :<0.01%
P/N : DRV2700: Industrial piezo driver with integrated 105-V boost converter

## Slide 4: Piezo Actuator Driver Circuit
Note: Use a 1:1 isolation transformer at out+ and out- pins to protect piezo actuator from external disturbances
Note: Use a Balun to Convert single ended o/p of DAC o/p to Differential signal

## Slide 5: 3. Voltage O/P DAC
P/N : DAC9881

## Slide 6: 4. Space Grade Microcontroller

## Slide 7
Space Grade Microcontroller Specs
P/N: MSP430FR5969
features
1) Core : 16 bit, 16MHz
2) Connectivity: I²C, SPI, UART, 40 GPIO
3)Memory: 256 KB FRAM, 8 KB SRAM
4)Voltage - Supply (Vcc/Vdd): 1.8V ~ 3.6V

## Slide 8: 5. Nano-positioning Sensor
A high-resolution position feedback system to continuously monitor the position of the optical component in both pitch and yaw axes is needed. This feedback should be accurate down to nanometer-level precision.
The Solution is : Capacitive sensor

## Slide 10
P/N: D-510.100

## Slide 11
6. Signal Conditioner

## Slide 12
P/N: E-509.E03

## Slide 13: Need For Signal Conditioner:
Removes Noise and amplifies sensor signal, Improves Range.
Improves Linearity
Eliminates Drift and Hysteresis when used in Closed loop operations
ILS Circuitry Maximizes Capacitive Sensor Linearity

## Slide 14: Alternate Signal Conditioner
P/N: AMP04ESZ
AMP04ESZ: Precision Instrumentation Amplifier
Wide gain range: 1 to 1000
Single-resistor gain set
Single pole Low pass Filter setting

## Slide 15
7. Data Acquisition (ADC)
Resolution (Bits):24
Sample rate (max) (ksps):128
Number of input channels: 4
Interface Type: Single-ended
Simultaneous Sampling
Multichannel configuration:
Input voltage range : (max) (V) : 4.5
Input voltage range (min) (V) : -1.5
SNR=115.2, ENOB=(SNR(dB)−1.76)/6.02​ = 18.81
P/N: ADS131A04

## Slide 16
Vresolution ​= Input Voltage Range​/ (2^ENOB)
Vresolution ​= 6​/(2^18.81)
Vresolution​ ≈ 18.25μV
5v corresponds to  150um
18.25μV corresponds to  0.547nm
The Data Acquisition System is capable of sub nm resolution measurement

## Slide 17
8. Control Algorithm
Proportional term addresses immediate deviations, but in cases where there are continuous disturbances(drift and Hysteresis) preventing the system from reaching the setpoint, the integral term is necessary to gradually eliminate the steady-state error by accumulating and responding to the persistent deviation over time.
u[k]= Kp​⋅e[k] + Ki​ *( i=0 to K ∑ ​e[i]⋅Ts​ )

## Slide 18: P I Tuning and Evaluation
Performance Evaluation
Stability Analysis:
  Evaluate the stability of the system by checking for overshooting, oscillations, and settling time. Adjust P and I gains accordingly.
Transient Response:
  Analyze the transient response of the system to step inputs. Ensure that the response is fast without introducing instability.
Steady-State Error:
  Fine-tune the integral gain to minimize steady-state error. This is particularly important in applications where accurate positioning is critical.
P I Controller Setup
Proportional (P) Control:
  Start with a proportional-only controller (PI with I term set to zero). Tune the proportional gain (Kp) to achieve a response that is fast but doesn't introduce excessive oscillations.
Integral (I) Control:
  Introduce the integral term gradually (increase Ki) to eliminate steady-state error. Be cautious not to introduce too much integral action, as it can lead to instability or overshooting.

## Slide 19: 9.Block Diagram
DAC
Piezo Actuator/s Fine steering Mirror
Piezo Driver
P.I, Micro Controller
Signal Conditioner
ADC
Non Contact Capacitive Sensors
EO Payload Electronics

## Slide 20: 10.Major BOM
SL No. | Description | Part No
1 | Fine Steering Mirror | P-FSM400MML
2 | Piezo Actuator Driver | DRV2700
3 | Voltage O/P DAC | DAC9881
4 | Space Grade Microcontroller | MSP430FR5969
5 | Single Electrode Capacitive Sensor | D-510.100
6 | 3 channel Signal Conditioner | E-509.E03
7 | Instrumentation Amplifier | AMP04ESZ
8 | Data Acquisition (ADC) | ADS131A04

## Slide 21: THE END
Submitted By: UR Nikhil Bhat
https://www.linkedin.com/in/nikhil-bhat-7121a8144/
+91 81618237278
nikhilbhat920@gmail.com

## Slide 22: Additional Info
Nanopositioner Z and tip/tilt stage with large aperture

## Slide 24: Digital Piezo Controller

## Slide 25: E-727 Digital Multi-Channel Piezo Controller

## Slide 26: Features:
=> 3 channel Cap sensing, signal conditioning and sensing via ADC
=> PZT Amplifier for 3 Axis Piezo nanopositioning,
=> DSP Controller with 4th order polynomial linearization for mechanics and electronics
=> Ethernet, USB, RS-232, serial SPI high-speed interface LabVIEW driver, shared libraries for Windows, and Linux